## Slide 1: Instruction List - an assembler type of language
Eelco van der Wal
Managing Director PLCopen
www.plcopen.org

## Slide 2: Examples of instruction fields
START: LD %IX1 (* PUSH BUTTON *)
ANDN %MX5 (* NOT INHIBITED *)
ST %QX2 (* FAN ON *)
Label
Operator
Operand
Comment
result := result OP operand

## Slide 3: Operator and Semantics
LD Set current result equal to operand
ST Store current result to operand location
S Set Boolean operand to 1
R Reset Boolean operand to 0

## Slide 4: Operator and Semantics
AND Boolean AND
& Boolean AND
OR Boolean OR
XOR Boolean Exclusive OR

## Slide 5: Operator and Semantics
ADD Addition
SUB Subtraction
MUL Multiplication
DIV Division

## Slide 6: Operator and Semantics
GT Comparison: >
GE Comparison: >=
EQ Comparison: =
NE Comparison: <>
LE Comparison: <=
LT Comparison: <

## Slide 7: Operator and Semantics
JMP Jump to label
CAL Call function block
RET Return from called function or
function block
) Evaluate deferred operation

## Slide 8: Function Block Invocation Examples
1. CAL with input list: CAL C10(CU:=%IX10, PV:=15)
2. CAL with load/store of inputs: LD 15 ST C10.PV LD %IX10 ST C10.CU CAL C10
3. Use of input operators:
LD 15 PV C10 LD %IX10 CU C10

## Slide 9
FB Type Operators
SR S1,R
RS S,R1
R_TRIG CLK
F_TRIG CLK
CTU CU,R,PV
CTD CD,LD,PV
CTUD CU,CD,R,LD,PV
TP IN,PT
TON IN,PT
TOF IN,PT