## Slide 1: Structured Text a high level language
Eelco van der Wal
Managing Director PLCopen
www.plcopen.org

## Slide 2: Operators in ST
Symbol Operation
(expression) Parenthesization
identifier(argument list) Function evaluation
Examples:
LN(A), MAX(X,Y), etc.
** Exponentiation
- Negation
NOT Complement

## Slide 3: Operators in ST
* Multiply
/ Divide
MOD Modulo
+ Add
- Subtract
< , > , <= , >= Comparison
= Equality
<> Inequality

## Slide 4: Operators in ST
& Boolean AND
AND Boolean AND
XOR Boolean Exclusive OR
OR Boolean OR

## Slide 5: assignment
A := B;

## Slide 6: assignment
A := B;
Datatype to Datatype
INT to INT
or
Analog_Channel_Configuration to Analog_Channel_Configuration

## Slide 7: assignment
A := B;
INT to INT
or
Analog_Channel_Configuration to Analog_Channel_Configuration
CV := CV+1;
C := SIN(X);

## Slide 8: Controlled repetition via iteration or selection
IF .. THEN .. ELSE
CASE
FOR
WHILE …
REPEAT UNTIL

## Slide 9: IF .. THEN .. ELSE
IF condition= true
THEN action1
ELSE action2 (condition not true)
IF raining THEN Stay_In ELSE Go_Out

## Slide 10: IF .. THEN .. ELSE
D := B*B - 4*A*C ; IF D < 0.0 THEN NROOTS := 0 ; ELSIF D = 0.0 THEN NROOTS := 1 ; X1 := - B/(2.0*A) ; ELSE NROOTS := 2 ; X1 := (- B + SQRT(D))/(2.0*A) ; X2 := (- B - SQRT(D))/(2.0*A) ; END_IF ;

## Slide 11: CASE : repetitive IF
CASE selector OF
selector_value : action
ELSE …..
END_CASE;

## Slide 12: CASE : repetitive IF
TW := BCD_TO_INT(THUMBWHEEL);
TW_ERROR := 0;
CASE TW OF 1,5: DISPLAY := OVEN_TEMP;
2: DISPLAY := MOTOR_SPEED; 3: DISPLAY := GROSS - TARE; 4,6..10: DISPLAY := STATUS(TW - 4);
ELSE DISPLAY := 0 ; TW_ERROR := 1;
END_CASE; QW100 := INT_TO_BCD(DISPLAY);

## Slide 13: FOR
SUM := 0 ;
FOR begin_value TO end_value DO
END_FOR ;

## Slide 14: FOR
SUM := 0 ;
FOR I := 1 TO 3 DO
FOR J := 1 TO 2 DO
SUM := SUM + J ; END_FOR ;
SUM := SUM + I ;
END_FOR ;

## Slide 15: FOR
J := 101 ;
FOR I := 1 TO 100 BY 2 DO IF WORDS[I] = 'KEY' THEN J := I ; EXIT ; END_IF ;
END_FOR ;

## Slide 16: WHILE
J := 1;
WHILE J <= 100 & WORDS[J] <> 'KEY' DO J := J+2 ;
END_WHILE ;

## Slide 17: REPEAT … UNTIL
J := -1 ;
REPEAT J := J+2 ; UNTIL J = 101 OR WORDS[J] = 'KEY' END_REPEAT ;

## Slide 18: EXIT and RETURN
The EXIT statement shall be used to terminate iterations before the termination condition is satisfied.
SUM := 0 ; FOR I := 1 TO 3 DO FOR J := 1 TO 2 DO IF FLAG THEN EXIT ; END_IF
SUM := SUM + J ; END_FOR ;
SUM := SUM + I ; END_FOR ;